KERMIT-09 Users guide


                                  FLEX-09 KERMIT
                                  --------------




     Author:      Jur van der Burg
                  Nettelhorst 56
                  2402 LS  Alphen aan den Rijn
                  The Netherlands
     Language:    C (Compiled with Introl (c) compiler)
     Version:     3.0
     Date:        July 1986




     KERMIT  for  FLEX  has it's roots in the UNIX version. It is enhanced in 
     several ways, such as data logging, server mode etc.

     It  should  run  on about any version of the FLEX-09 (tm) or SK*DOS (tm) 
     operating  system.  It requires 48K of memory. Hardware dependent things 
     are kept in the files FLK.H and FLIO.C .

     FLEX-09 KERMIT has most of the features specified in the KERMIT Protocol 
     Manual.


































                                - 1  -



     KERMIT-09 Users guide


     1. Remote and Local Operation

          KERMIT  programs can be run in two ways, remote and local. A remote 
          Kermit  is usually running on a mainframe, which you have CONNECTed 
          to  through  a PC or other computer. When KERMIT runs remotely, all 
          file  transfer  is done over the job's controlling terminal line -- 
          the same line over which you logged in, and to which you would type 
          interactive  commands.  What  the system thinks is your terminal is 
          really  another  computer, usually a microcomputer, running its own 
          copy of Kermit.

          When  KERMIT  is  in  "local  mode",  file transfer is done over an 
          external  device,  such  as  a microcomputer's serial communication 
          port, or an assigned terminal line on a mainframe. The local Kermit 
          is  connected  in  some  way  (like a dialout mechanism) to another 
          computer,  again  running its own copy of Kermit. A local Kermit is 
          in  control  of the screen, a remote Kermit has no direct access to 
          it.

          Microcomputer   KERMITs   usually  run  in  local  "mode",  whereas  
          mainframe  Kermits usually need to be given some special command to 
          run  in  local  mode.  Some  commands  make  sense  only for remote 
          Kermits,  others  only  for  local,  still  others can be used with 
          either. Local and remote operation of KERMIT is shown schematically 
          here:

      Micro is Local, Mainframe is Remote:


                  Communication Line           (Packets)
                 +-------------------/  /-----------------+  Other terminals
                 !                                        !  !  !  !
                 !                                        !  !  !  !
       Micro     !     LOCAL                  Mainframe   !  !  !  !  REMOTE
      +----------+----------+                +------------+--+--+--+--------+
      !   Serial Port       !                !            !                 !
      !                     !                !            !                 !
      !                     !                !            !                 !
      !  +---------------+  !                !            Your job's        !
      !  ! Packets: 724  !  !                !            terminal line     !
      !  !               !  !                !                              !
      !  ! File: FOO.BAR !  !                !                              !
      !  +---------------+  !                !                              !
      !   Screen            !                !                              !
      !                     !                !                              !
      +---------------+-----+                +------------------------------+
                      !
                      ! (Commands)
                      !
         +------------+---------+
          \       Keyboard       \
           +----------------------+
                      You







                                - 2  -



     KERMIT-09 Users guide


          The  KERMIT  program on the micro is a local Kermit. It can control 
          the  screen,  the  keyboard,  and  the port separately, thus it can 
          update  the  screen  with  status  information, watch for interrupt 
          signals   from   the   keyboard,   and   transfer  packets  on  the  
          communications port, all at the same time.

          The KERMIT program running on the mainframe is a remote Kermit. The 
          user  logs  in  to  the mainframe through a terminal port. The host 
          computer  cannot  tell  that the user is really coming in through a 
          microcomputer.  The  keyboard,  screen,  and port functions are all 
          combined  in  user's  mainframe  terminal  line. Therefore a remote 
          Kermit  is  cut  off  from  your  screen  and  keyboard during file 
          transfer.

          A  KERMIT server is always remote, and must get its commands from a 
          local  KERMIT.  The  following  descriptions  will  indicate when a 
          command must be remote or local.

     2. Command Interface

          The FLEX-09 implementation has an interactive keyword-style command 
          interface,  modeled after that of the DEC VAX/VMS operating system, 
          which is roughly as follows:

          In response to the "Kermit-xx>" prompt you may type a keyword, such 
          as SEND, RECEIVE, or EXIT, possibly followed by additional keywords 
          or  operands,  each  of which is called a field. You can abbreviate 
          keywords  (but  not  file  names)  to  any  length  that makes them 
          distinguishable  from  any  other keyword valid for that field. The 
          command  is  terminated  by  a carriage return. Before the carriage 
          return  is  typed,  the command can be edited using RUBOUT or other 
          command  editing  keys.  Finally, the same command is entered again 
          with  a  minimum  of keystrokes, with each field abbreviated to its 
          shortest unique length.

     3. Notation

          In the command descriptions, the following notation is used:

          anything
                    A  parameter  -  the symbol is replaced by an argument of 
                    the specified type (number, filename, etc).

          [anything]
                    An   optional  field.  If  omitted,  it  defaults  to  an  
                    appropriate value.

          number
                    A   whole  number,  entered  in  hexadecimal  or  decimal  
                    notation.

          character
                    A  single  character,  entered  literally, or as a number 
                    (perhaps  decimal  or hexadecimal) representing the ASCII 
                    value of the character.

          file-spec
                    A  file  specification, i.e. the name of a file, possibly 
                    including a drive number or other qualifying information, 

                                - 3  -



     KERMIT-09 Users guide


                    and  possibly  containing  "wildcard" or pattern-matching 
                    characters to denote a group of files.

          ^X
                    A  control  character  may  be written using "uparrow" or 
                    "caret"  notation,  since  many  systems  display control 
                    characters  this  way. Control characters are produced by 
                    holding  down  the  key marked CTRL or Control and typing 
                    the appropriate character, e.g. X.

          Commands  are  shown  in  upper  case,  but  can  be entered in any 
          combination of upper and lower case.

     4. Summary of KERMIT Commands

          Here  is  a  brief list of KERMIT commands as they are found in the 
          FLEX-09  KERMIT program. The following sections will describe these 
          commands in detail.

          For exchanging files:
              SEND, RECEIVE, GET

          For connecting to a remote host:
              CONNECT, SET LINE, SET CONFIGURATION, SET BAUD, SET DUPLEX,
              SET HANDSHAKE, SET ESCAPE, SET PROMPT, SET LOG

          For acting as a server:
              SERVER

          For talking to a server:
              BYE, FINISH, GET, SEND

          Setting nonstandard transmission and file parameters:
              SET BLOCK_CHECK_TYPE, SET DEBUG, SET DELAY, SET FILETYPE,
              SET INCOMPLETE, SET WARNING, SET CONFIGURATION, SET RETRY,
              SET END_OF_LINE, SET START_OF_PACKET, SET PACKET_LENGTH,
              SET TIMEOUT, SET PADDING, SET PADCHAR, SET QUOTE,
              SET REPEAT_QUOTE, SET EIGHT_BIT_QUOTE, TAKE

          For interrupting transmission:
              Control-X, Control-Z

          Getting information:
              HELP, STATISTICS, SHOW, Control-D

          For recording the history of a file transfer operation:
              SET DEBUG LOG

          For non-protocol file capture or transmission:
              SET LOG, TRANSMIT

          Leaving the program:
              EXIT, QUIT

          If  you have a file called KERMIT.INI in your default or home disk, 
          KERMIT  will  execute  an automatic TAKE command on it upon initial 
          startup.  KERMIT.INI  may contain any KERMIT commands, for instance 
          SET   commands   to   configure   KERMIT   to  various  systems  or  
          communications media.

                                - 4  -



     KERMIT-09 Users guide



     5. The SEND Command

        Syntax: SEND filespec [filespec2] [filspec3...]

          The  SEND  command  causes  a  file or file group to be sent to the 
          other  system. The filespec may contain the commonly used wild-card 
          characters  '*'  and/or  '?',  where  '*' stands for a string match 
          (including  null)  and '?' stands for a single character match. Use 
          of  wildcard  characters  is the most common method of indicating a 
          group  of  files  in  a  single file specification. For instance if 
          FOO.BAS  is  a  single  file, a BASIC program named FOO, then *.BAS 
          might  be a group of BASIC programs. If filespec1 contains wildcard 
          characters  then  all  matching  files  will be sent, in directory-
          listing  order  by name. If a file can't be opened for read access, 
          it  will  be  skipped. There may be a total of twenty files or file 
          groups specified.

        SEND Command General Operation


          Files  will  be sent with their filename and filetype (for instance 
          FOO.BAR,  no  device  or  directory  field, no generation number or 
          attributes).  If  communication  line parity is being used (see SET 
          CONFIGURATION),  the  sending  KERMIT  will  request that the other 
          KERMIT  accept  a special kind of prefix notation for binary files. 
          This  is  an  advanced feature, and not all KERMITs have it; if the 
          other  KERMIT  does  not  agree  to  use this feature, binary files 
          cannot be sent correctly.

        SEND Remote Operation


          If   you   are  running  KERMIT  remotely  (for  instance,  from  a  
          microcomputer),  you  should  "escape  back"  to  your local Kermit 
          within  a  reasonable  amount of time and give the RECEIVE command. 
          Don't  take  more  than about one minute to complete the switch, or 
          KERMIT  may  "time  out"  and give up (in that case, you'll have to 
          CONNECT back to the remote system and reissue the SEND command).

        SEND Local Operation


          If  you're running KERMIT locally, for instance on a microcomputer, 
          you  should have already run KERMIT on the remote system and issued 
          either a RECEIVE or a SERVER command.

          Once  you  give KERMIT the SEND command, the name of each file will 
          be  printed  on your screen as the transfer begins, and information 
          will  be  displayed  to  indicate  the  packet  traffic.  When  the 
          specified operation is complete, the program will sound a beep, and 
          the  status  of  the  operation  will  be  indicated by the message 
          Complete, Interrupted, or Failed.

          If  you  see  many  packet  retry  indications,  you  are  probably 
          suffering  from  a noisy connection. You may be able to cut down on 
          the  retransmissions  by  using  SET  PACKET_LENGTH to decrease the 
          packet length; this will reduce the probability that a given packet 
          will  be  corrupted  by  noise,  and  reduce  the  time required to 

                                - 5  -



     KERMIT-09 Users guide


          retransmit  a  corrupted  packet.  If  you notice a file being sent 
          which  you do not really want to send, you may cancel the operation 
          immediately  by  typing  either Control-X or Control-Z. If your are 
          sending  a  file group, Control-X will cause the current file to be 
          skipped,  and KERMIT will go on to the next file, whereas Control-Z 
          will  cancel  sending  the entire group and return you to KERMIT-09 
          command level.

     6. The RECEIVE Command

        Syntax:  RECEIVE [filespec]

          The  RECEIVE command tells KERMIT to wait for the arrival a file or 
          file  group  sent  by a SEND command from the other system. If only 
          one  file  is being received, you may include the optional filespec 
          as  the  name to store the incoming file under; otherwise, the name 
          is  taken  from the incoming file header. If the name in the header 
          is  not  a legal file name on the local system, KERMIT will attempt 
          to  transform  it to a legal name. If an incoming file has the same 
          name as an existing file, KERMIT will either overwrite the old file 
          or  else  try to create a new unique name, depending on the setting 
          of FILE WARNING.

          If  you  have SET CONFIGURATION with parity, then 8th-bit prefixing 
          will  be  requested. If the other side cannot do this, binary files 
          cannot  be  transferred  correctly.  The  sending  KERMIT  may also 
          request that repeated characters be compressed.

          If  an  incoming  file does not arrive in its entirety, KERMIT will 
          normally  discard it; it will not appear in your directory. You may 
          change  this  behavior  by  using  the command SET INCOMPLETE KEEP, 
          which will cause as much of the file as arrived to be saved in your 
          directory.

        RECEIVE Remote Operation


          If your are running KERMIT remotely, you should escape back to your 
          local  Kermit  and give the SEND command. You should do this within 
          about  one  minute,  or  KERMIT  may  time out and give up; if this 
          happens,  you can CONNECT back to the remote system and reissue the 
          RECEIVE command.

        RECEIVE Local Operation


          If you are running KERMIT locally, you should already have issued a 
          SEND command to the remote KERMIT, and then escaped back to KERMIT-
          09  (not  SERVER  --  use  the  GET command to receive files from a 
          KERMIT server).

          As  files  arrive,  their names will be shown on your screen, along 
          with a continuous display the packet traffic.

          If  a  file  begins  to arrives that you don't really want, you can 
          attempt to cancel it by typing Control-X; this sends a cancellation 
          request to the remote Kermit. If the remote Kermit understands this 
          request  (not  all implementations of Kermit support this feature), 
          it  will comply; otherwise it will continue to send. KERMIT-09 will 

                                - 6  -



     KERMIT-09 Users guide


          detect  this situation and send an error packet. If a file group is 
          being sent, you can request the entire group be cancelled by typing 
          Control-Z.


     7. GET

        LOCAL ONLY -- Syntax: GET remote-filespec [filespec2...]

          The GET command requests a remote KERMIT server to send the file or 
          file  group  specified  by  remote-filespec.  Note  the distinction 
          between  the  RECEIVE  and GET commands: RECEIVE puts KERMIT into a 
          passive  wait  state,  whereas  GET  actively  sends a command to a 
          server.

          The  GET  command  can  be  used  only when KERMIT is local, with a 
          KERMIT  server  on  the  other end of the line. This means that you 
          must  have  CONNECTed  to  the  other system, logged in, run KERMIT 
          there,  issued  the  SERVER  command, and escaped back to the local 
          KERMIT.

          The  remote  filespec  is  any  string  that  can  be  a legal file 
          specification  for the remote system; it is not parsed or validated 
          locally.  As  files  arrive,  their names will be displayed on your 
          screen,  along  with a continuous indication of the packet traffic. 
          As  in  the RECEIVE command, you may type Control-X to request that 
          the  current  incoming file be cancelled, Control-Z to request that 
          the entire incoming batch be cancelled.

          If  the  remote KERMIT is not capable of server functions, then you 
          will  probably  get  an  error  message  back from it like "Illegal 
          packet  type".  In this case, you must connect to the other Kermit, 
          give a SEND command, escape back, and give a RECEIVE command.

     8. SERVER

        Syntax: SERVER

          The  SERVER  command instructs KERMIT to cease taking commands from 
          the keyboard and to receive all further instructions in the form of 
          KERMIT packets from another system. A KERMIT server must be remote; 
          that  is,  you  must  be  logged  in  to the system through another 
          computer,  such  as a microcomputer. In addition, your local KERMIT 
          should  have  commands for communicating with remote servers; these 
          include GET, FINISH, and BYE.

          After  issuing  this  command, escape back to your local system and 
          issue  SEND,  GET,  BYE,  FINISH, or other server-oriented commands 
          from  there. If your local KERMIT does not have a BYE command, then 
          it  does  not  have  the  full ability to communicate with a KERMIT 
          server  and  you should not put the remote KERMIT into SERVER mode. 
          If  your  local KERMIT does have a BYE command, use it to shut down 
          and  log  out  the  KERMIT  server  when  you are done with it. The 
          KERMIT-09  server  can  also  be  shutdown  by  typing Control-X or 
          Control-Z. Then the server will stop after the timeout.

          Any  nonstandard  parameters  should  be selected with SET commands 
          before putting KERMIT in server mode, in particular the block check 
          type and special file modes.

                                - 7  -



     KERMIT-09 Users guide



     9. BYE

        LOCAL ONLY -- Syntax: BYE

          When  running as a local Kermit talking to a KERMIT server, use the 
          BYE  command  to  shut  down and log out the server. This will also 
          close any debugging log files and exit from the local KERMIT.

     10. FINISH

        LOCAL ONLY -- Syntax: FINISH

          When  running  as  a local Kermit talking to a remote KERMIT server 
          use  the FINISH command to shut down the server without logging out 
          the remote job, so that you can CONNECT back to it.

     11. FLEX

        Syntax: FLEX command

          Execute  the specified command on the local system -- on the system 
          where  KERMIT  to  which  your  are typing this command is running. 
          These  commands  provide  some  local  file  management  capability 
          without  having  to leave the KERMIT program, which is particularly 
          useful  on microcomputers. Be sure that the programs you run reside 
          in the utility command space ($C100 - $C6FF).

          FLEX DELETE filespec   Delete the specified file or files.

          FLEX CAT [filespec]    Provide a directory listing of the specified
                                 files.

     12. CONNECT

        LOCAL ONLY -- Syntax: CONNECT [terminal-designator]

          Establish  a  terminal connection to the system at the other end of 
          the  communication  line.  On a microcomputer, this is normally the 
          serial  port.  On  a mainframe, you will have to specify a terminal 
          line  number  or  other  identifier,  either in the CONNECT command 
          itself, or in a SET LINE command. If a log file was opened (see SET 
          LOG)  then  the  data  will  be  buffered  in memory, which will be 
          written  to  disk  if it becomes full. Handshaking is provided (see 
          SET  HANDSHAKE).  Get back to the local KERMIT by typing the escape 
          character followed by a single character "command".














                                - 8  -



     KERMIT-09 Users guide


          Several single-character commands are possible:

            C      Close the connection and return to the local KERMIT.
            H      Show availability.
            S      Show status of the connection.
            B      Send a BREAK signal.
            0      (zero) Send a NUL (0) character.
            Q      Quit logging session transcript.
            R      Resume logging session transcript.
            ?      List all the possible single-character arguments.
            ^      (or whatever you have set the escape character to be)
                   Typing the escape character twice sends one copy of it
                   to the connected host.
            other  Rings the bell.

          You  can  use  the  SET ESCAPE command to define a different escape 
          character,  and  SET  CONFIGURATION,  SET  BAUD,  SET  DUPLEX,  SET 
          HANDSHAKE to establish or change those parameters.

     13. HELP

        Syntax: HELP [subject] [sub-subject]

          Typing  HELP  alone  prints  a  brief  summary  of  KERMIT  and its 
          commands.  Help  about a particular topic can be obtained by giving 
          it as a parameter. The HELP data file will be searched on the drive 
          KERMIT-09 was loaded from.

     14. EXIT, QUIT

        Syntax: EXIT
        or:     QUIT

          Exit  from  KERMIT.  QUIT  is a synonym for EXIT. If a log file was 
          used  with  CONNECT,  and  the buffer still contains data, then the 
          buffer will we written to disk before terminating KERMIT-09.

     15. The SET Command

        Syntax: SET parameter [option] [value]

          Establish  or  modify  various  parameters  for  file  transfer  or 
          terminal connection.

          When   a   file   transfer   operation   begins,  the  two  KERMITs  
          automatically  exchange  special  initialization messages, in which 
          each  program  provides  the  other  with certain information about 
          itself.  This  information includes the maximum packetsize it wants 
          to  receive, the timeout interval it wants the other KERMIT to use, 
          the number and type of padding characters it needs, the end-of-line 
          character  it  needs  to  terminate each packet (if any), the block 
          check type, the desired prefixes for control characters, characters 
          with  the  "high  bit"  set,  and  repeated characters. Each KERMIT 
          program  has  its own preset "default" values for these parameters, 
          and  you  normally  need  not  concern  yourself with them. You can 
          examine  their  values  with  the  SHOW command; the SET command is 
          provided  to  allow you to change them in order to adapt to unusual 
          conditions.


                                - 9  -



     KERMIT-09 Users guide


          The following parameters may be SET:

            BAUD             Set the speed of the current communications port
            BLOCK_CHECK_TYPE Packet transmission error detection method
            CONFIGURATION    Character parity to use
            DEBUG            Mode or log file
            DELAY            How long to wait before starting to send
            DUPLEX           For terminal connection, full (remote echo) or
                             half (local echo)
            EIGHT_BIT_QUOTE  Character to use for binary file transfer if
                             parity used
            END_OF_LINE      End of line character
            ESCAPE           Character for terminal connection
            FILETYPE         For setting ascii or binary file type.
            HANDSHAKE        Selecting flow control characters, like XON/XOFF
            INCOMPLETE       What to do with an incomplete file
            LINE             Terminal line to use for terminal connection or
                             file transfer
            LOG              CONNECTion logging file
            PACKET_LENGTH    Length of a packet
            PADDING          Number of padding characters
            PADCHAR          Padding character
            PROMPT           Prompt of the local KERMIT
            QUOTE            Character used to transfer control characters
            REPEAT_QUOTE     Character to use for data compression
            RETRY            How many times to retry a packet before give up
            START_OF_PACKET  Start of packet character
            TIMEOUT          Time to wait for a packet
            WARNING          File conflict warning flag


       SET BAUD

        Syntax: SET BAUD number

          Set  or change the baud rate (approximate translation: transmission 
          speed  in bits per second) on the currently selected communications 
          device.  In  simple  FLEX systems the only allowable baud-rates are 
          300 and 1200. Other interfaces may provide a complete range.

       SET BLOCK_CHECK_TYPE

        Syntax: SET BLOCK_CHECK_TYPE number

          KERMIT  normally  uses a 1-character block check, or "checksum", on 
          each  packet.  The  sender  of  the packet computes the block check 
          based  on  the  other  characters  in  the packet, and the receiver 
          recomputes  it  the same way. If these quantities agree, the packet 
          is  accepted  and  the transmission proceeds. If they disagree, the 
          packet is rejected and transmitted again.

          However,  the  block  check  is  not  a  foolproof  method of error 
          detection. The normal single-character KERMIT block check is only a 
          6-bit  quantity  (the low order 8 bits of the arithmetic sum folded 
          upon  itself).  With only six bits of accuracy, the chances are one       
              6
          in 2  -- that is, 1/64 -- that an error can occur which will not be 
          detected  in  the  checksum,  assuming  that all errors are equally 
          likely.

                                - 10 -



     KERMIT-09 Users guide



          You can decrease the probability that an error can slip through, at 
          the   expense   of   transmission  efficiency,  by  using  the  SET  
          BLOCK_CHECK_TYPE  command  to  select  more  rigorous  block  check 
          methods.  Note  that  all  three methods will detect any single-bit 
          error, or any error in an odd number of bits.

          The options are:

            1-CHARACTER-CHECKSUM:

                    The normal single-character 6-bit checksum.

            2-CHARACTER-CHECKSUM:

                    A  2-character,  12-bit checksum. Reduces the probability 
                    of an error going undetected to 1/4096, but adds an extra 
                    character to each packet.

            3-CHARACTER-CRC:

                    A  3-character,  16-bit  Cyclic  Redundancy  Check, CCITT 
                    format.  In addition to errors in any odd number of bits, 
                    this  method  detects double bit errors, all error bursts 
                    of  length  16  or  less,  and  more  than  99.99% of all 
                    possible longer bursts. Adds two extra characters to each 
                    packet.

          The  single  character  checksum has proven to be quite adequate in 
          practice,  much  more effective than straightforward analysis would 
          indicate,  since  all  errors  are not equally likely, and a simple 
          checksum  is  well  suited to catching the kinds of errors that are 
          typical  of  telecommunication  lines.  The other methods should be 
          requested only when the connection is very noisy.

          Note  that the 2- and 3-character block checks are not available in 
          all  versions  of  KERMIT;  if  the  other KERMIT is not capable of 
          performing  the  higher-precision  block  checks, the transfer will 
          automatically use the standard single-character method.

       SET DEBUG

        Syntax: SET DEBUG options [file]

          Record  the  packet  traffic, either on your terminal or in a file. 
          Options are:

          ON              Display each incoming and outgoing packet
                          (lengthy).

          OFF             Don't display debugging information (this is the
                          default). If debugging was in effect, turn it off
                          and close any open debug log file.

          LOG             Log the information to the specified file.

          During  data  transfer,  debugging  can  be  toggled  on and off by 
          pressing Control-D. If a log file was opened, it will be closed.


                                - 11 -



     KERMIT-09 Users guide


       SET DELAY

        Syntax: SET DELAY number

          Specify  how  many  seconds to wait before sending the first packet 
          after  a  SEND  command.  Use when remote and SENDing files back to 
          your local Kermit. This gives you time to "escape" back and issue a 
          RECEIVE  command.  The  normal delay is 5 seconds. In local mode or 
          server mode, KERMIT does not delay before sending the first packet.

       SET DUPLEX

        Syntax: SET DUPLEX keyword

          For  use when CONNECTed to a remote system. The keyword choices are 
          FULL  and  HALF. FULL means the remote system echoes the characters 
          you  type,  HALF  means  the  local system echoes them. FULL is the 
          default,  and  is  used  by  most  hosts.  HALF  is  necessary when 
          connecting  to  IBM  mainframes.  Half duplex is also called "local 
          echo".

       SET ESCAPE

        Syntax: SET ESCAPE character

          Specify  or  change  the character you want to use to "escape" from 
          remote  connections  back  to  KERMIT.  This  would  normally  be a 
          character  you  don't  expect  to  be  using  on the remote system, 
          perhaps  a control character like ^[, ^], ^^, or ^_. KERMIT-09 uses 
          the up-arrow ('^') by default. After you type the escape character, 
          you  must  follow  it by a single-character "argument", such as "C" 
          for  Close  Connection.  The  arguments are listed above, under the 
          description of the CONNECT command.

       SET FILETYPE

        Syntax: SET FILETYPE parameter

          Establish file-related parameter. This may be either ASCII for text 
          files  or  BINARY  for  non-text  files.  This  is a very important 
          command  if  you  intend  to transfer binary files, but is normally 
          unnecessary for transmitting textual files.

       SET HANDSHAKE

        Syntax: SET HANDSHAKE start stop

          For  communicating  with  full  duplex  systems.  System-level flow 
          control is not necessary to the KERMIT protocol, but it can help to 
          use  it  if  the same method is available on both systems. The most 
          common  type of flow control on full duplex systems is XON/XOFF. If 
          the  KERMIT  input  buffer is filled up to 250 characters, the stop 
          character is sent. If the buffer becomes empty and contains only 10 
          characters,  the  start  character  will  be send. The defaults for 
          start is XON (17), and for stop XOFF (19).





                                - 12 -



     KERMIT-09 Users guide


       SET INCOMPLETE

        Syntax: SET INCOMPLETE option

          Specify  what  to  do  when  a  file  transfer  fails  before it is 
          completed.  The  options are DISCARD (the default) and KEEP. If you 
          choose KEEP, then if a transfer fails to complete successfully, you 
          will be able to keep the incomplete part that was received.

       SET LINE

        Syntax: SET LINE terminal-designator

          Specify the terminal line to use for file transfer or CONNECT. This 
          command  is  found  on  mainframe  KERMITs,  which  normally run in 
          "remote  mode"  using  their  own  controlling  terminal  for  file 
          transfer.  Specifying  a  separate  line puts the program in "local 
          mode". If the line is specified as 'REMOTE', the communication will 
          revert to the job's controlling terminal.

       SET CONFIGURATION

        Syntax: SET CONFIGURATION number

          Parity   is  a  technique  used  by  communications  equipment  for  
          detecting  errors  on  a per-character basis; the "8th bit" of each 
          character acts as a check bit for the other seven bits. KERMIT uses 
          block  checks  to  detect errors on a per-packet basis, and it does 
          not  use  character  parity. However, some systems that KERMIT runs 
          on,  or  equipment  through which these systems communicate, may be 
          using  character  parity.  If  KERMIT  does  not  know  about this, 
          arriving  data  will  have  been  modified and the block check will 
          appear to be wrong, and packets will be rejected.

          If  parity is being used on the communication line, you must inform 
          both  KERMITs,  so  the  desired  parity  can  be added to outgoing 
          characters,  and  stripped  from  incoming  ones. SET CONFIGURATION 
          should  be used for communicating with hosts that require character 
          parity  (IBM mainframes are typical examples) or through devices or 
          networks that add parity to characters that pass through them. Both 
          KERMITs   should   be   set  to  the  same  parity.  The  specified  
          configuration parity is used both for terminal connection (CONNECT) 
          and file transfer (SEND, RECEIVE, GET).

          The choices for SET CONFIGURATION are:

            0.  Seven data bits, even parity and two stop bits.
            1.  Seven data bits, odd parity and two stop bits.
            2.  Seven data bits, even parity and one stop bit.
            3.  Seven data bits, odd parity and one stop bit.
            4.  Eight data bits, no parity and two stop bits.
            5.  Eight data bits, no parity and one stop bit (default).
            6.  Eight data bits, even parity and one stop bit.
            7.  Eight data bits, odd parity and one stop bit.

          Eight  bits  means no parity is affecting the data, and the 8th bit 
          of  each  character  can  be used for data when transmitting binary 
          files.


                                - 13 -



     KERMIT-09 Users guide


          If  you  have  set  to  use parity then advanced versions of KERMIT 
          (including  KERMIT-09)  will  request  that  binary  files  will be 
          transferred  using  8th-bit-prefixing.  If  the KERMIT on the other 
          side knows how to do 8th-bit-prefixing (this is an optional feature 
          of  the KERMIT protocol, and not all implementations of KERMIT have 
          it),  then  binary files can be transmitted successfully. If eight-
          bits  communication  is  specified,  8th-bit-prefixing  will not be 
          requested.

       SET EIGHT_BIT_QUOTE

        Syntax: SET EIGHT_BIT_QUOTE character

          What  character to use to process eight_bit bytes over a line using 
          only  seven data bits. The sending KERMIT will ask the other KERMIT 
          whether it can handle a special prefix encoding for characters with
          the  eighth  bit  on,  using  the  eight_bit_quote  character. This 
          character  should  be  distinct from the REPEAT_QUOTE character and 
          the  QUOTE  character.  The default is "&" (38). There should be no 
          reason to change this.

       SET END_OF_LINE

        Syntax: SET END_OF_LINE character

          The ASCII character to be used as a line terminator for packets, if 
          one  is  required  by the other system, carriage return by default. 
          You  will  only have to use this command for systems that require a 
          line  terminator  other than carriage return. The character must be 
          specified as a hexadecimal number.

       SET LOG

        Syntax: SET LOG filespec

          Create  a  transcript  of  a  CONNECT session, when running a local 
          KERMIT connected to a remote system, in the specified file. Logging 
          can be "toggled" by typing the connect escape character followed by 
          Q  (Quit  logging) or R (Resume logging). Session-logging is useful 
          for   recording   dialog   with  an  interactive  system,  and  for  
          "capturing"  from  systems that don't have KERMIT. No guarantee can 
          be made that the file will arrive correctly or completely, since no 
          error  checking  takes  place.  The  log file will be closed if the 
          filespec is a dash ("-").

       SET PACKET_LENGTH

        Syntax: SET PACKET_LENGTH number

          Maximum  packet  length  to  send  between  10  and  94  (decimal). 
          Shortening  the  packets  might  allow  more of them to get through 
          through without error on noisy communication lines. Lengthening the 
          packets increases the throughput on clean lines.

       SET TIMEOUT

        Syntax: SET TIMEOUT number

          How many seconds to wait for a packet before trying again.

                                - 14 -



     KERMIT-09 Users guide



       SET PADDING

        Syntax: SET PADDING number

          How much padding to send before a packet, if the other side needs
          padding. Default is no padding.

       SET PADCHAR

        Syntax: SET PADCHAR character

          What  kind  of  padding  character to send. Default is NUL (0). The 
          character must be specified as a hexadecimal number.

       SET QUOTE

        Syntax: SET QUOTE character

          What  printable character to use for quoting of control characters. 
          This   character   should  be  distinct  from  the  EIGHT_BIT_QUOTE  
          character  and the REPEAT_QUOTE character. The default is "#" (35). 
          There should be no reason to change this.

       SET REPEAT_QUOTE

        Syntax: SET REPEAT_QUOTE character

          What  character  to  use  to  process  repeat count characters. The 
          sending  KERMIT  will  ask the other KERMIT whether it can handle a 
          special   prefix   encoding  for  repeated  characters,  using  the  
          repeat_quote  character. This character should be distinct from the 
          EIGHT_BIT_QUOTE  character  and the QUOTE character. The default is 
          "~" (126). There should be no reason to change this.

       SET RETRY

        Syntax: SET RETRY number

          Set the maximum number of retries for how many times to try sending 
          a  particular  packet  before  giving up, normally 10. If a line is 
          very noisy, you might want to increase this number.

       SET START_OF_PACKET

        Syntax: SET START_OF_PACKET character

          The  start-of-packet  character  is the only control character used 
          "bare"  by  the  KERMIT  protocol. It is Control-A by default. If a 
          bare  Control-A  causes problems for your communication hardware or 
          software,  you  can  use this command to select a different control 
          character  to  mark  the  start  of a packet. You must also set the 
          start_of_packet  character  at  the  KERMIT  on  the  other  system 
          (providing  it has such a command). The character must be specified 
          as a hexadecimal number.





                                - 15 -



     KERMIT-09 Users guide


       SET WARNING

        Syntax: SET WARNING keyword

          Enable  or  disable the warning if an incoming file already exists, 
          where  the  keyword  must  be either ON or OFF. When set to ON (the 
          default)  and  an  incoming file already exists, an attempt will be 
          made  to  store  the  file under a new and unique name. When set to 
          OFF, an existing file will be overwritten.

     16. SHOW

        Syntax: SHOW option

          The  SHOW command displays the values of the parameters settable by 
          the SET command. If the option is ALL, then a complete display will 
          be provided.

     17. STATISTICS

        Syntax: STATISTICS

          Give  statistics  about  the most recent file transfer, such as the 
          total  number  of  characters  transmitted, the effective baud rate 
          (only if a hardware clock is available), and so forth.

     18. TAKE

        Syntax: TAKE filespec

          Execute  KERMIT  commands  from  the  specified  file. The file may 
          contain any valid KERMIT commands, including other TAKE commands.

     19. TRANSMIT

        Syntax: TRANSMIT filespec

          Send the contents of the specified file to the other system "bare", 
          without  protocol, packets, error checking, or retransmission. This 
          command   is  useful  for  sending  standard  logon  or  connection  
          sequences,  or  to  send  commands to a smart modem, or for sending 
          files  to  systems that don't have KERMIT. No guarantee can be made 
          that  the  target  system  will  receive  the  file  correctly  and 
          completely. When receiving a file, the target system would normally 
          be  running  a  text editor in text collection mode. The tranferred 
          data will be displayed on the screen if DEBUG is on.














                                - 16 -