QL-KERMIT                                          Edition DRAFT, 4-May-87









                         QL-KERMIT - Documentation
                         =========================




  1.  Introduction
  ----------------


  This  documentation briefly describes my (with acknowlegements to others -
  see the  comments  at  the  front  of  the main program) implementation of
  Kermit on the Sinclair QL.  It is assumed  that  the  reader is reasonably
  familiar with Kermit and how to use a "standard" Kermit program.

  The first release version of QL-Kermit (referred to from here on as 'QLK')
  comprises about 120K bytes of  C  source,  compiling to about 55K bytes of
  object code.  Although the object will run on  a standard unexpanded QL, a
  memory expansion (preferably to the maximum 640K) and at  least  one  disc
  drive  is  an essential configuration for compilation or development work.
  The Metacomco C Development Kit is also required.

  Refer to  the Building QL-Kermit  section  for information on building QLK
  from source.



























                                    Page 1




  QL-KERMIT                                          Edition DRAFT, 4-May-87





  2.  Capabilities at a Glance
  ----------------------------


         Local operation                         Yes
         Remote operation                        No
         Transfer text files                     Yes
         Transfer binary files                   Yes
         Wildcard send                           No
         ^X/^Z interruption                      Yes
         Filename collision avoidance            No
         Can time out                            Yes
         8th-bit prefixing                       Yes
         Repeat count prefixing                  No
         Alternate block checks                  No
         Terminal emulation                      Yes
         Communications settings                 Yes
         Transmit BREAK                          No
         IBM mainframe communication             No
         Transaction logging                     No
         Session logging                         No
         Raw transmit                            No
         Act as server                           No
         Talk to server                          Yes
         Advanced server functions               No
         Advanced commands for servers           Limited
         Local file management                   Unnecessary
         Handle file attributes                  No
         Command files                           Yes
         Command macros                          No
         XON/XOFF flow control                   No
         Split baud rates                        No


  I have not implemented some  of  these  features for various reasons:  (a)
  they are not relevant to  my  intended  use  of  QLK;   (b)  they would be
  impossible  to  implement  on  the QL hardware (e.g. transmit BREAK);  (c)
  they may be implemented at a later date.

  Note:  At present I have  only tested QLK transferring files to and from a
  BBC  running  Lancs-Kermit  (version  1.45).   Therefore   I   have   only
  extensively  tested  features which are used  by  this  configuration.   I
  cannot guarantee that other facilities work well enough, if at all.












                                    Page 2




  QL-KERMIT                                          Edition DRAFT, 4-May-87





  3.  Using the program
  ---------------------


  Assuming that the binary version of QLK has been obtained or built, it can
  be run by using the EXEC command (or, if you have Toolkit or Super Toolkit
  fitted, EX).  The console window  will  clear, and the version string will
  be displayed.  At this point it will  look  for  a startup file which will
  typically  contain  a series of Kermit commands to configure QLK  for  the
  intended   application.   As   supplied   the   file   searched   for   is
  "flp1_qlk_take"; it can  be  altered  to look for a different file or on a
  different device by changing the symbol DFTAKE in the header file ker_h.

  When this startup file has  ended,  or if none is found, the prompt "QLK>"
  will be displayed.  (Fairly) standard Kermit commands  can now be entered;
  these are listed in the next section.  The  following  control keys can be
  used to control and edit command lines:

    F1   (HELP)  When pressed at the  beginning  of  a  field, indicate what
         this  field  needs  to  be  completed with, or display  a  list  of
         options.

    F3   (DELETE LINE)  Abandon the current  command  entirely.  ^U can also
         be used.

    F4   (COMPLETE/DEFAULT)  If pressed at the beginning  of a field, supply
         and display the default value  for that field (if any).  If pressed
         in the middle of a 'keyword'  field, complete the field if what has
         been  typed  already is valid and unambiguous.   If  these  do  not
         apply, the key is ignored.  ESC can also be used.

    F5   (DELETE CHARACTER)  Delete the character to the left of the cursor.
         The standard QL CTRL-LEFT, or ^H, can also be used.

    ^R   (REDISPLAY)  Replay the current command  line  (e.g.  if the screen
         has been corrupted by another job's output).

  Commands  may  be  entered in either upper or lower case  (or  indeed  any
  mixture of the two).

  Note that CTRL-C can be  used  to switch the keyboard input to another job
  (assuming  that  QLK  has been started by  EXEC  or  EX);  this  makes  it
  unnecessary to include commands in QLK for local file management.

  During file transfer, the following control keys are recognised:

    ^X   (INTERRUPT FILE)  If sending,  end transmission of the current file
         and send an EOF packet with a Discard request.  Note that since the
         current version of QLK does  not  support  the  sending of multiple
         files, this key has an identical action to ^Z.

         If receiving, request the remote  system  to abort the transmission
         of  the current file and continue with  the  next  one  (if  it  is


                                    Page 3




  QL-KERMIT                                          Edition DRAFT, 4-May-87


         sending multiple files).

    ^Z   (INTERRUPT BATCH)  If sending, end transmission of the current file
         and send an EOF packet with a Discard request, followed by  an  EOT
         packet to end the batch.

         If receiving,  request  the remote system to abort the transmission
         of the current file and  not  send  any  more  (if  it  is  sending
         multiple files).

    ^T   (FORCE TIMEOUT)  If pressed while QLK is waiting for a packet to be
         received, the wait will be  abandoned and a timeout simulated, thus
         forcing QLK to resend the previous  packet or acknowledgment.  This
         is  useful for manually unjamming the deadlock  caused  by  a  lost
         packet, if for some reason the timeout facility is not being used.

    ^E   (FATAL ERROR)   If  for  some  reason  the  remote  system does not
         support  ^X/^Z interruption, these control keys will have no effect
         in stopping  the  transfer.  In this case pressing ^E will cause an
         Error packet to be  sent  with an appropriate message - this should
         cause any remote system to stop.





































                                    Page 4




  QL-KERMIT                                          Edition DRAFT, 4-May-87





  4.  Commands
  ------------


  The commands available in QLK  are  listed  here,  with  the  syntax and a
  description for each.  Note that a command or required keyword need not be
  typed in full - only enough characters need be typed to make what is meant
  unambiguous.

  UPPERCASE   is   to  be  typed  literally;  lowercase  indicates  variable
  parameters; [brackets] indicate optional parameters.  Possible options are
  seperated by ','s.



  CONNECT

  This enters terminal emulation on the currently selected serial line.  The
  screen  will clear and the  cursor  reappears  in  the  top  left  corner.
  Terminal emulation  is  extremely  dumb,  with  no support for any special
  features of the QL screen or any  standard  video  terminal.   The special
  keys recognised are:

    F2   (EXIT)  This returns to Kermit command mode.

    F3   (NULL)  This sends the ASCII code 0.

    F4   (^C)  This sends the ASCII code 3.

    F5   (DEL)  This sends the ASCII code 127.

   ENTER (EOL) Sends the currently defined  end  of line sequence, as set by
         SET ENTER.

  All other keys are sent  to the serial line.  If the LOCAL-ECHO option has
  been set to ON, the key  press  is  also  echoed  to the screen.  ENTER is
  always echoed as a newline regardless of the setting of the  end  of  line
  sequence.



  DO command-line

  This is equivalent to REMOTE HOST in  most  other  versions of Kermit.  It
  sends the specified 'command-line' to  be  executed  by the remote server,
  and displays the results on the QL screen.



  EXIT

  Exits the Kermit program.



                                    Page 5




  QL-KERMIT                                          Edition DRAFT, 4-May-87




  FINISH

  Sends a command to a remote server requesting it to exit server operation,
  and return to Kermit command mode.



  GET remote [local]

  Asks the remote server to  send  a file.  'remote' is the file to be sent,
  in the filename syntax appropriate to the  remote  system.  'local' is the
  QL filename to store it under; if omitted, the  name that the remote sends
  in  the File-Header packet will be translated to a suitable  QL  filename.
  If 'local'  is  not  given, or if it is given but it includes no QL device
  prefix, the file will be  stored  on the current DESTINATION device.

  Note that if the server  sends  multiple  files  as  a result of including
  wildcards  in 'remote', then 'local' must not be given, otherwise  the  QL
  will overwrite  the  just-received  file  each  time a new one is started.
  However, QLK does not check this, and  it  may  even  be  useful  in  some
  applications  (e.g.  to  see  the  files on the screen, give "scr_" as the
  local name).



  HELP

  Displays  a summary of the control keys available in command, transfer and
  terminal modes.



  QUIT

  Equivalent to EXIT.



  RECEIVE [local]

  Waits for  a  file  to  be  sent from a remote non-server.  'local' is the
  filename that it will be stored under;  if  omitted,  the  name  that  the
  remote sends in the  File-Header  packet  will  be used (as for GET).  The
  remarks under GET regarding multiple files also apply here.



  SEND local [remote]

  Sends a file to a remote, whether a server or not.  'local' is the QL file
  to be sent.  'remote', if  given,  is  the  name  that will be sent in the
  File-Header packet; if omitted, the local name  will  be used.  If 'local'
  has no QL device prefix, the current SOURCE device will be used.



                                    Page 6




  QL-KERMIT                                          Edition DRAFT, 4-May-87




  SET parameter option
  SET sub-section parameter option

  Controls various options of the Kermit program.  See the next section.



  SHOW [what]

  Displays  the  current  Kermit  settings and parameters.  'what' indicates
  what is to be shown, it may be:

         ALL             Everything except VERSION
         COMMUNICATION   Settings relating to the serial ports and
                         terminal emulation
         DEVICES         Current default devices (see SET DEVICE)
         FILE            Settings relating to file transfer
         PREFIX          The current quote characters
         SYSTEM          Settings which don't fit in anywhere else
         TRANSFER        Protocol parameters, timeouts, etc.
         VERSION         The current QLK version

  If 'what' is omitted, ALL is assumed.



  TAKE filename

  Read and execute Kermit commands from a file.  No file suffix is enforced,
  but the suggested one is "_take".  If the filename  given has no QL device
  prefix, then the current TAKE device will be used.

  If the TAKE-ECHO option is  set to ON, command lines read from a TAKE file
  will be listed on the screen  prior  to them being executed.  They will be
  preceded  by  "TAKE-n>",  where  n  is the TAKE  file  nesting  level,  to
  distinguish them from commands typed at the keyboard.

  The TAKE command can be  used within a TAKE file, thus allowing them to be
  nested to a maximum of 10 levels.  However, if an invalid command is read,
  or if an error occurs during  a  file  transfer,  the entire stack of TAKE
  files will be abandoned if the TAKE-ABORT option is set to ON.  (This does
  not include a transfer interruption initiated by ^X or ^Z; however it does
  include a fatal error initiated  by  ^E).  This can be disabled by setting
  the TAKE-ABORT option to OFF.












                                    Page 7




  QL-KERMIT                                          Edition DRAFT, 4-May-87





  5.  The SET command
  -------------------


  The  options  that can be controlled by the SET command are  given  below.
  Note that SEND,  RECEIVE,  FILE  and  DEVICE  are  logically sub-sections,
  although they are described here as if they were seperate options.



  BAUD speed

  Set the baud rate for the currently set serial  line.  The valid rates are
  those listed in the  QL  manual.   The setting on entry is for the current
  speed to be retained (as set by the SuperBasic BAUD command).



  CONTROL-QUOTE char

  Sets the character that QLK will prefix control characters in packets that
  it sends with, and indicate to the remote system that it will do so.  This
  is normally '#', but can  be  changed for special applications.  Note that
  QLK, when receiving packets, always uses the  quote  character  the remote
  has asked it to.



  DEBUGGING OFF,ON,FULL

  Sets the debugging level.  OFF  is  the initial setting, no information is
  displayed.  ON causes messages regarding file manipulation and packet read
  failures to be displayed.  FULL in addition displays information regarding
  the switcher state, and the contents of all incoming and outgoing packets.



  DELAY time

  Sets the wait, in seconds, between the SEND command being accepted and the
  file transfer starting.  If connected  to  another  microcomputer  Kermit,
  this  gives  time for the RECEIVE command to be typed on the other system.
  The initial setting is 5 seconds.

  While QLK is  waiting ("Pausing" displayed) the wait can be interrupted by
  pressing any key; the transfer will start immediately.



  DEVICE DESTINATION device

  Sets the default destination device for file transfers.  If the opening of
  the file for the GET or RECEIVE commands fails due to a "Not found" error,


                                    Page 8




  QL-KERMIT                                          Edition DRAFT, 4-May-87


  this string will be prepended  to  the file name and another attempt made.
  No  checks are made on the validity  of  this  device,  and  the  trailing
  underscore must  be  included.   Note that if the first attempt at opening
  the file fails for some  reason other than "Not found" (e.g. "In use") the
  addition of the device prefix will  not  be done and an error message will
  be issued immediately.

  The initial setting is "flp2_".



  DEVICE SOURCE device

  Sets the default source device  for  file  transfers.   If  the local file
  given in the SEND command is not found, this device  will  be prepended to
  the name given  and  another  attempt  made  to   find  it.   The  remarks
  applying to DESTINATION regarding other errors also apply here.

  The initial setting is "flp2_".



  DEVICE TAKE-FILE device

  Sets the default source device for command files read by the TAKE command.
  The initial setting is "flp1_".



  EIGHT-BIT-QUOTE char

  Sets the character that QLK  will  use  for  8th-bit  quoting,  if  it  is
  necessary and the remote system agrees to use the same character.  This is
  normally  '&', but can be changed for special applications.



  ENTER CR,LF,CRLF,LFCR

  Sets the character(s) that will  be transmitted in terminal emulation mode
  when the ENTER key is pressed.   CR  is  Carriage Return (ASCII 13); LF is
  Line Feed (ASCII 10).  If it is set to  CRLF  or  LFCR then two characters
  will be transmitted in succession.  The initial setting is CR.



  FILE INCOMPLETE DELETE,KEEP

  Controls  what  happens  to  a  partially  received  file if a transfer is
  abandoned (by a ^X or  ^Z  interrupt)  or  fails  (due to an error or a ^E
  interrupt).  If set to DELETE, the file is deleted; if  set  to  KEEP, the
  partial file is retained.  The initial setting is DELETE.






                                    Page 9




  QL-KERMIT                                          Edition DRAFT, 4-May-87




  FILE NAME NORMAL,UNTRANSLATED

  Controls  whether  file  names sent or received in File-Header packets are
  translated  to or from a  standard  QL  format  before  use.   If  set  to
  UNTRANSLATED, when sending the name sent will be identical to the name the
  QL file  was opened with (not necessarily that given on the command line);
  for receive, the name contained in the packet will be used for the QL file
  (but the DESTINATION device will still be prepended if necessary).

  If set to  NORMAL,  the  QL  filename  will  be  translated to or from the
  "standard"  Kermit  format  (as  described  in  the Protocol Manual).  The
  conversions applied for sending are:

    (a)  The QL device prefix is stripped off
    (b)  Lowercase letters are converted to uppercase
    (c)  The last '_', if any, is changed to a '.'.

  The conversions applied on receiving are:

    (a)  Uppercase letters are converted to lowercase
    (b)  Any '.'s are converted to '_'s.

  Note that, if a remote name is  given  in  the  SEND command, this will be
  sent verbatim in the packet, even if NORMAL mode is set.   Similarly, if a
  local name is given for GET or RECEIVE, this will not be translated (apart
  from the possible addition of the DESTINATION device).

  The initial mode is NORMAL.



  FILE SUFFIX [string]

  Sets  a  possible  suffix string which is added to files sent by  QLK,  to
  identify their source when  they  are  stored on a remote filestore.  If a
  'string' is given, this (preceded  by  a '_') will be appended to outgoing
  filenames before undergoing translation.  This suffix will not be added if
  a remote name is given explicitly, or if UNTRANSLATED mode is set.

  If 'string' is not given, no suffix   will be added.  Initially, no suffix
  is set.

  An example may be in  order  here  to clarify the interaction between send
  translation and suffix addition.  If the SOURCE device  is  set to "flp2_"
  and the SUFFIX to "ql", then the command:

         SEND main_c

  will  search  first  for  "main_c"   (and  not  find  it)  and  then  find
  "flp2_main_c" (assuming that it exists  on  that  device).   Firstly,  the
  suffix will be added to that name, giving "flp2_main_c_ql", then this will
  be  translated  to  the  Kermit  format  -  making  the  name  sent in the
  File-Header packet "MAIN_C.QL".



                                   Page 10




  QL-KERMIT                                          Edition DRAFT, 4-May-87


  If no file suffix is  set,  the  name  "flp2_main_c" will be translated to
  Kermit format, thus sending "MAIN.C".

  If UNTRANSLATED mode had been set, then the name  sent in the packet would
  be "flp2_main_c".



  FILE TYPE ASCII,BINARY

  Controls whether end-of-line translation  is  applied to file data sent or
  received during a transfer.  If set  to  BINARY,  no  translation is done;
  this  allows object files, etc. to be sent and received  exactly  as  they
  appear in the filestore.

  If set to ASCII, end-of-line translation is done as follows:

  For sending, a QL end  of line (LF, ASCII 10) is sent in the packet as the
  prefix sequence "#M#J", assuming that the  control-quote in use is '#'.  A
  carriage return (ASCII 13) encountered in the  file  will be sent as "#M".
  For receiving, "#M" is ignored and "#J" is written to the file as LF.

  This has the effect (assuming that the option is  set  correctly  at  both
  ends  of the link) of allowing a printable text file on the sending system
  to become  a  printable  text  file on the receiving system, regardless of
  what means the other system uses to represent end of line.

  Note that the ASCII/BINARY setting has  no  bearing on whether the 8th-bit
  of a byte is sent, with quoting or  otherwise.   It  affects  end  of line
  translation only.

  The initial setting is ASCII.



  LINE [1,2]

  Sets the serial port to  be used for data transfer.  '1' selects ser1, '2'
  selects ser2.  If '1' or '2'  is  not  given,  the old line is freed (thus
  allowing another job to use that serial  port)  but no new line is opened.
  Initially, no line is set.



  LOCAL-ECHO OFF,ON

  Controls whether keys pressed in terminal mode are echoed to the screen by
  the QL, or by the  remote  computer.   Note  that  if it is set to ON, the
  ENTER key is always echoed  as  a newline regardless of the setting of the
  ENTER action.  The initial setting is OFF.



  PADDING [amount [character]]

  Controls whether padding is inserted after a transmitted packet,  to allow


                                   Page 11




  QL-KERMIT                                          Edition DRAFT, 4-May-87


  for  communication line delays or remote system requirements.  'amount' is
  the number  of  pad  characters that are to be transmitted; the default is
  0 (no padding).  'character' is the character to be used (in decimal); the
  default is NUL (ASCII 0).   If  'amount'  and  'character' are omitted, no
  padding will be done.

  Note that the amount of  padding  and  the  character  used are subject to
  negotiation  in  the  Send-Init  packet exchange.  The algorithms used are
  explained later.



  PARITY NONE,ODD,EVEN,MARK,SPACE

  Selects the parity setting that  will  be used by the QL for transmission,
  and checked on reception.  The initial setting is NONE.

  The  parity  setting  interacts  with  whether  8th-bit  quoting  will  be
  specified or requested in the Send-Init packet  exchange.   See  the notes
  later regarding this exchange.



  RECEIVE END-OF-LINE code

  Specifies  the end-of-line character that  QLK  will  request  the  remote
  system to  terminate  a  packet  with.   This is specified in decimal; the
  initial setting is Carriage Return (ASCII 13).   Note  that  QLK  does not
  require  any end of packet marker, so this option is redundant.   It  also
  appears pointless to allow this character to be specified in the Send-Init
  exchange, since  if a different terminator to the default was required the
  Send-Init packet or its acknowledgement could not be received!



  RECEIVE MARKER code

  Specifies, in decimal, the character  that  QLK  will look for to indicate
  the start of an incoming packet.  The initial setting is SOH (ASCII 1).



  RECEIVE PACKET-LENGTH length

  Specifies the maximum packet length  that  QLK  will  request  the  remote
  system to send.  The initial setting is  the  maximum  of  94.  A sensible
  minimum is about 30, but this is not enforced by QLK.



  RECEIVE TIMEOUT time

  Specifies the time, in seconds,  that QLK will wait for an incoming packet
  (if the timer is enabled).  The  initial  setting is 20.  The timeout used
  is subject to Send-Init negotiation.



                                   Page 12




  QL-KERMIT                                          Edition DRAFT, 4-May-87




  RETRIES number

  Sets the number of times  that  QLK  will  retransmit  a  packet  when the
  expected  reply  is  not  received succesfully.  This includes packet read
  timeouts  (if  the timer is  enabled),  timeouts  forced  by  ^T,  packets
  received with a bad checksum  or  unexpected  reception  of  a  previously
  received  packet.   If  this  limit  is  exceeded, the transaction will be
  aborted.   Note  that the retry limit applies  to  the  reception  of  one
  particular packet, and not the total number of retries in a transaction.

  The initial setting is 5.



  SEND END-OF-LINE code

  Specifies the end-of-line character that QLK will terminate a packet with.
  This is specified in decimal;  the  initial  setting  is  Carriage  Return
  (ASCII  13).  The remarks under the corresponding RECEIVE option regarding
  the specification of  this  parameter in the Send-Init exchange also apply
  here.



  SEND MARKER code

  Specifies, in decimal, the character  that  QLK  will transmit to indicate
  the start of a packet.  The initial setting is SOH (ASCII 1).



  SEND PACKET-LENGTH length

  Specifies the maximum packet length  that  QLK  will  send  to  the remote
  system.  The initial setting is the maximum of 94.  A sensible  minimum is
  about  30,  but  this is not enforced by QLK.  This length is  subject  to
  Send-Init negotiation.



  SEND TIMEOUT time

  Specifies the time, in seconds,  that  QLK  will  ask the remote system to
  wait for an incoming packet, if it has a  timeout  facility.   The initial
  setting is 20.



  TAKE-ABORT OFF,ON

  Controls whether TAKE files are abandoned when a command or transfer error
  occurs.   If it is set to ON, the entire stack of TAKE files (i.e. the one
  containing the  command  causing the error, as well as any that called it)
  is abandoned and control  returns  to the keyboard prompt.  If set to OFF,


                                   Page 13




  QL-KERMIT                                          Edition DRAFT, 4-May-87


  the error is ignored and execution  continues with the next command in the
  TAKE file.  See the description of the TAKE command for more information.

  The initial setting is ON.



  TAKE-ECHO OFF,ON

  Controls whether command lines read from a  TAKE  file  are  echoed on the
  screen  before execution.  If set to ON, they are listed with  a  "prompt"
  identifying their  source and the current level of TAKE file nesting.  See
  the TAKE command for more information.

  The initial setting is ON.



  TIMER OFF,ON

  Controls  whether  QLK  will  time out if a packet being waited for is not
  received within the specified or negotiated time.  If set to OFF, QLK will
  never time out and will  wait  indefinitely  if  a  packet does not arrive
  (execpt that a timeout can be simulated with ^T).  If  set  to ON, timeout
  processing will be performed normally.  The initial setting is ON.

































                                   Page 14




  QL-KERMIT                                          Edition DRAFT, 4-May-87





  6.  Notes on Send-Init parameter negotiation
  --------------------------------------------


  Certain parameters relating to the  file  transfer  that  is just about to
  start  are  negotiated  between  the  two  sides in the  Send-Init  packet
  exchange.   The algorithms QLK uses to derive  the  parameters  eventually
  used in  the  file  transfer  are  described  here.   Note that "send" and
  "receive"  here  refer  to  packets and not necessarily file  data.   Also
  observe that some Kermit implementations  may  well  ignore the parameters
  requested in the exchange, and either impose their  own  defaults  or some
  compromise (as QLK does in some cases).



  (a)  Packet length

  QLK asks the remote system  to  send it packets no longer than the RECEIVE
  PACKET-LENGTH setting, but will not fail if  for  some reason this request
  is ignored.  Initially the packet length that it sends  is  that specified
  by SEND PACKET-LENGTH; however if the remote system requests it to  send a
  shorter packet, QLK will do that.  The eventual length used is the minimum
  of the QLK setting and the remote request.



  (b)  Timeout

  QLK requests the remote system to time out (if it is capable  of doing so)
  after the SEND TIMEOUT interval.  The initial timeout QLK uses is that set
  by  RECEIVE  TIMEOUT; if the remote system specifies that QLK should use a
  longer interval, it  will do so.  The eventual receive timeout used is the
  maximum of the QLK setting and the remote request.



  (c)  Padding amount

  QLK does not require  padding  on  receive,  and  always specifies that no
  padding should be sent to it.  Initially the amount  of  padding sent, and
  the  character  used, are those set by PADDING; after the exchange,  if  a
  greater number of  padding  characters  are  requested by the remote, that
  number will be used.  The padding character  sent is always that specified
  in the packet.



  (d)  End of line

  QLK  sends  the  first  packets  with  the  terminator   defined  by  SEND
  END-OF-LINE, and then uses that requested by the  remote,  if  given.  QLK
  does  not  require a terminator on incoming packets, but requests that set
  by RECEIVE END-OF-LINE for completeness.


                                   Page 15




  QL-KERMIT                                          Edition DRAFT, 4-May-87





  (e)  Control quote

  The quote characters are not  used  until  he  Send-Init exchange is over,
  therefore  no  initial  setting is relevant.  QLK will inform  the  remote
  system that it will  send  data  using the character set by CONTROL-QUOTE;
  for receiving data it will use the quote character the remote specifies.



  (f) 8th-bit quote

  The current parity setting interacts  with  8th-bit  quote  negotiation as
  follows:

  If the parity setting is  NONE,  QLK need not do 8th-bit quoting, but will
  do so if the remote requires it.   In  this case, the quote character used
  is that specified by the remote, if it requires  8th-bit  prefixing  to be
  done.  If the remote need not do 8th-bit quoting either, then it  will not
  be  done.   The  character  specified  by EIGHT-BIT-QUOTE is irrelevant in
  this case.

  If the parity setting is one  which  permits  only 7-bit transmission, QLK
  will specify that it needs  to  do 8th-bit prefixing.  The quote character
  used will depend on which side initiates the exchange:

  If QLK sends the Send-Init packet, it will request that 8th-bit quoting is
  to be done using the character currently  set.  If the remote replies that
  it  will  use  the  same character, or it  will  optionally  do  so,  that
  character will be used for the transaction.

  In the case where QLK reads the Send-Init packet and acknowledges with its
  own parameters, if the remote has specified optional quoting then QLK will
  indicate that it must use  the  set  character.  If the remote specifies a
  quote character, thus indicating that it must prefix,  then  QLK  will use
  the character specified too.



  (g)  Other parameters

  QLK supports only checksum type 1, and assumes that the remote will agree.
  Repeat  count prefixing is not supported; nor are any exotic features such
  as file attributes, sliding windows or long packets.


  Note  that, if any parameters are not specified by the remote system (i.e.
  if it sends a short  parameter  packet),  QLK  will  continue  to  use the
  initial settings as they were at the start of the transaction.







                                   Page 16




  QL-KERMIT                                          Edition DRAFT, 4-May-87





  7.  Building QL-Kermit from source
  ----------------------------------


  To  build  QLK  from  source  requires  a little more than the standard QL
  configuration.  The Metacomco C Development Kit is essential, and at least
  one disc drive.  Expansion memory, if available,  would  greatly  speed up
  compilation; the maximum of 640K is preferred.

  The source files required are:

         main_c                  Main program and global data
         cmd_c                   Command processor
         fns_c                   Protocol support routines
         swit_c                  Protocol state switcher
         us1_c                   User commands
         us2_c                   The SET command
         term_c                  Terminal emulation
         sbr_c                   General subroutines

         ker_h                   General definitions
         cmd_h                   Command processor definitions
         usr_h                   User command and option definitions

         kermit_link             Linker control file

  Also  required,  as  supplied  with  the  C  Development Kit, are stdio_h,
  ctype_h, qdos_h and fcntl_h.

  The device names in the  #include  statements and linker control file have
  been set assuming that a full configuration  of 640K of memory and 2 discs
  is available and that the source and object  files  will  be  stored  on a
  RAMdisc, which must be of at least 450 sectors.  The final executable file
  is best written to disc, since if the RAMdisc is made big enough  to  hold
  this  as  well  the  C  compiler will be a very tight fit in the remaining
  memory.  The system include files are assumed to be on flp1_.

  For other configurations, the files  will have to be edited to reflect the
  disposition of source and system files.

  Whatever the configuration, when all  the  source files have been compiled
  they can be linked with the Linker command line:

         -with DEV1_kermit -nolist -prog DEV2_kermit_exec

  where DEV1 is the device that kermit_link resides  on,  and  DEV2  is  the
  device that the executable file is to be written to.  Note that the Linker
  control file may also have  to  be  edited  to reflect the device that the
  object files are held on.

  After this has been done, Kermit can be run using EXEC (or EXEC_W).




                                   Page 17




  QL-KERMIT                                          Edition DRAFT, 4-May-87





  8.  Acknowledgments
  -------------------


  Thanks are due to:

  Robert Coughlan, lately of Liverpool  University, for writing the original
  version of QL-Kermit and making it available via Lancaster.

  The Lancaster Kermit Distribution Service,  and  especially  Alan Phillips
  whose  excellent  implementation of BBC-Kermit inspired me to  provide  it
  with something to talk to.

  David Gordon; for programming help,  QL  advice  and the loan of a machine
  and supporting bits.

  The writers of the original  C-Kermit,  from  which many of the algorithms
  used  in  QLK are taken;  also  the  original  developers  of  the  Kermit
  protocol.

  Sir Clive Sinclair; for taking  a  great  CPU,  building  a set of totally
  inadequate  hardware  around  it and  making  the  result  available  very
  cheaply.